## Slide 1: Edge AI-Based Grape Leaf Disease Detection
ESP32-S3 Real-Time Vineyard Monitoring System
Academic / Industry Project Presentation
December 2025

## Slide 2: Project Motivation & Objective
• Need for early disease detection in vineyards
• Limitations of cloud-based monitoring (latency, cost, connectivity)
• Objective: Develop a low-cost, real-time edge AI system
• Fully autonomous operation without cloud dependency

## Slide 3: System Overview
• Edge AI device deployed directly in vineyard
• ESP32-S3 microcontroller with camera
• On-device deep learning inference
• Periodic monitoring with ultra-low power consumption

## Slide 4: Hardware Platform
• ESP32-S3 (Dual-core LX7 @ 240 MHz)
• 16 MB Flash, 8 MB PSRAM
• OV3660 camera module (320×240, JPEG)
• USB-C power and programming

## Slide 5: Software Stack
• ESP-IDF v5.3.3
• ESP-DL deep learning framework
• Arduino ESP32 Camera Library (hybrid approach)
• FreeRTOS-based real-time execution

## Slide 6: Development Methodology
• Phase 1: Isolated component testing
• Phase 2: Iterative system integration
• Phase 3: Hybrid architecture and optimization
• Continuous profiling and debugging

## Slide 7: AI Model Architecture
• ESPDet-Pico lightweight object detector
• INT8 quantized model (491 KB)
• Input: 224×224 RGB images
• Output: Bounding boxes and confidence scores

## Slide 8: Inference Pipeline
1. Image capture (JPEG)
2. JPEG decode to RGB888
3. Resize/crop to model input
4. AI inference on ESP32-S3
5. Post-processing and detection output

## Slide 9: Memory Management Strategy
• Model weights stored in DRAM
• Camera buffers allocated in PSRAM
• JPEG compression reduces memory usage by 94%
• <10% PSRAM utilization during runtime

## Slide 10: Key Technical Challenges
• Cache coherency conflicts (PSRAM vs Flash)
• Limited DRAM availability
• Camera initialization instability
• Real-time performance constraints

## Slide 11: Key Innovations
• Load AI model before camera initialization
• Hybrid Arduino + ESP-IDF architecture
• JPEG-based capture pipeline
• Optimized memory hierarchy usage

## Slide 12: Performance Results
• Inference time: 135–138 ms
• End-to-end pipeline: ~182 ms
• Frame rate: 5.3–5.5 FPS
• Stable real-time operation

## Slide 13: Detection Accuracy
• 5–7 detections per frame
• Confidence range: 24–59%
• Conservative detection behavior
• Low observed false positives

## Slide 14: Power Efficiency
• Active power: ~300 mW
• Sleep power: ~10 mW
• Average power: ~20 mW
• >500 hours operation on 10 Ah battery

## Slide 15: System Stability
• Zero crashes during testing
• No memory leaks detected
• Stable thermal behavior
• Suitable for long-term deployment

## Slide 16: Applications & Use Cases
• Early grape leaf disease detection
• Vineyard health monitoring
• Solar-powered edge deployments
• Low-cost scalable sensor networks

## Slide 17: Limitations & Future Work
• Improve detection confidence via retraining
• Add data logging and wireless connectivity
• Disease classification and severity estimation
• Multi-sensor environmental integration

## Slide 18: Conclusions
• Demonstrated feasibility of edge AI on ESP32-S3
• Achieved real-time, low-power disease detection
• Cost-effective and scalable solution
• Strong foundation for commercial deployment